## Slide 1: Analog synthesis of a Sine wave using a pure digital FPGA chip
Giulia Gioachin
Flavio Galaverna

## Slide 2
About the Project

## Slide 3: General Scheme
ROM
PLL
PULSE GENERATOR
COUNTER
BINARY COMPARATOR
SHIFT REGISTER
INTERFACE LOGIC
DAC
EN
CLK
PWM
Vout
ANALOG INTERFACE
Vout
1
2
3
4

## Slide 4: First Mode PWM Technique
ROM
PLL
PULSE GENERATOR
COUNTER
BINARY COMPARATOR
EN
CLK
PWM
ANALOG INTERFACE
Vout
1
2
3

## Slide 5: Pulse Width Modulation
The PWM (Pulse Width Modulation) technique allows to program the duty cycle of a periodic signal

## Slide 6
The PWM (Pulse Width Modulation) technique allows to program the duty cycle of a periodic signal
How does PWM generate a Sine Wave?
Pulse Width Modulation

## Slide 7
A 32-bit counter generates an output (Tick) every 1000 clock posedge.
If Tick is equal to 1 the memory read one data
ROM (Read Only Memory):
(32x64) bits
64 hexadecimal values belonging to a sine wave with amplitude between 0 and 1000
Allocated in a B-RAM in FPGA
Read Only Memory (ROM)
Clock 200 MHz
Tick
ROM data

## Slide 8
A Binary Comparator (the heart of the PWM block) compares the ROM data values with a 32-bit counter:
ROM data > counter  1
Counter > ROM data  0
In this way the duty cycle changes and the time in which the signal is 1 increases with the increase of the sine value.
Sine wave with PWM
Sine

## Slide 9
PLL  Phase Locked Loop to provide a 200 MHz clock as input
IP-ROM  a ROM with the same size to the previous one to replace it
IP Blocks
Clock 100 MHz
Clock 200 MHz

## Slide 10
To visualize the Sine output as an analog output it is possible to use a simulator  LTspice
Built a circuit as
A voltage generator (V4) able to read a file with the time (on sec) and the sine values after the PWM technique ( the digital sine values are multiplied by 3.3V)
A resistance of 50 Ohm
A capacity of 400 nF
An operational amplifier (LT1178A)
Displaying the Sine Wave using LTspice

## Slide 11
Blue line is the output from the RC circuit
Red line is the output from the OP-AMP
Displaying the Sine Wave using LTspice

## Slide 12
Some constraints are used:
Position for the input ports (En and Clk100) and output port (Sine)
An input clock of 100 MHz, with a duty cycle of 50%
A capacity of 20 pF at the output
A 10 ns delay to all input ports
Project implementation on FPGA
B-RAM

## Slide 13: Second Mode DAC
TRANSMISSION INTERFACE
TRASMITTER SIMULATION
dac_enable
CLK
1
3
2
ROM
PLL
PULSE GENERATOR
DAC
Vout

## Slide 14
CLR: set all the data on the DAC REGISTER to 0 (not used in the project)
LD: enables data recording on the DAC REGISTER
CS: enables data shifting on the SERIAL REGISTER
CLK: allows synchronus transmission
SDI: serial data input
Digital to Analog Converter (DAC)

## Slide 15
NOT SYNTHESIZEBLE ON THE FPGA CHIP
SIPO 12 BIT SHIFT REGISTER
12 BIT SHIFT REGISTER
SDI
CLK
1
2
3
4
12
I_data
CS
LD
The DAC BEHAVIOURAL simulation
4
The DAC serial interface implementation
SYSTEM VERILOG CODE

## Slide 16
The FPGA set up
SIMULATION OF A REAL TRANSMITTER
TRANSMITTER SIMULATION
NEED TO TRANSMIT THE DATA CORRECTLY
TRANSMISSION INTERFACE
TARGET
IMPLEMENTED MODULE
SYNTHESIZEBLE ON THE FPGA CHIP
VERILOG CODE
Transmitter simulation
COUNTER
1 BYTE SHIFT REGISTER
RST
CLK
1
2
3
4
Data_bus
32
SO
5
LD_pdata

## Slide 17: TRANSMISSION INTERFACE
COUNTER
1 BYTE SHIFT REGISTER
RST
CLK
1
2
3
4
CS
5
LD_pdata
LD
BEHAVIOURAL SIMULATION OF THE TRASNMITER SIMULATION MODULE
TEST BENCH CODE FOR THE TRASMISSION INTERFACE MODULE

## Slide 18
BEHAVIOURAL SIMULATION OF THE TRASMISSION INTERFACE MODULE

## Slide 19
BEHAVIOURAL SIMULATION OF THE TOP LEVEL MODULE
TEST BENCH CODE FOR THE TOP LEVEL MODULE
USING VERILOG TASKS AND A PYTHON SCRIPT IS POSSIBLE TO WRITE THE DATA IN A ASCII FILE AND PLOT THEM